今天的生产面临需要更广泛的控制解决方案使操作更加灵活的压力，因此，GE Fanuc 智能设备提供系列90-30 PLC来提供从简单继电器替换到复杂中档自动化控制的多种功能。系列90-30有超过100个离散量和模拟量I/O模块以及一个创新结构和模块化设计，可以完全满足您的应用需求，并且随着您企业的增长而进行系统扩展。

产品描述

CPU模块

系列90-30 CPU对于需要较少I/O数量的入门级应用，可以采用嵌入在背板上的90-30 CPU，使得所有槽用于I/O模块。高性能的CPU是基于 Intel 的386EX处理器以得到快速计算和大量吞吐。它们最多能控制4096个I/O，高性能CPU最小用户内存为32K，能用多种标准语言进行编程。新型CPU374有一个运行在133 Mhz主频的AMDSC520处理器。除了能高速处理以外，系列90-30CPU374还提供带内置交换机的两个10/100M以太网端口（RJ- 45）。CPU374两个内置以太网口共用一个IP地址。CPU374以太网端口能自适应波特率，可以采用以太网直连或级连电缆。
CPU374支持SRTP服务器和以太网全局数据广播（EGD）协议。CPU374与EZ程序存储设备兼容，它能使用户无需计算机就能下载程序和组态。
CPU374布尔量执行速度为0.15milliseconds/K，它有240Kbyte的可组态内存，并且可以用梯形图、C语言或StateLogic?语言编程。CPU374最多可支持4096个远程和本地I/O。

电源模块
系列90-30电源模块依照CPU的性能分为单电源、故障安全电源和容错电源。高级诊断和内置智能开关熔丝也是它所拥有的性能。您可以选择我们新型的冗余系列90-30电源模块

分布式I/O通信模块
系列90-30有许多通信选项，包括以太网、Genius、Series 90 协议（SNP）和Modbus RTU。

I/O模块
系列90-30其真正的特点在于它的I/O。它有超过38个不同的离散量I/O类型和17个模拟量I/O类型，包括高速计数器、I/O处理器、可编程协处理器、温度控制、伺服运动控制器和PC协处理器等模块。

特殊模块
特殊模块包括热电偶模块、RTD模块、毫伏/应变仪模块、顺序事件记录模块、隔离模拟量模块、带调制解调器的通讯模块和一个气动阀输出模块。

可编程软件
系统90-30可选编程软件可以是梯形图逻辑、SFC、“C”或者状态逻辑。C语言编程使用户能处理复杂的计算，而这些计算一度只能由大型昂贵的PLC来执行。

选型表:

| IC693ACC300 | Input Simulator Module |
| --- | --- |
| IC693ACC300LT | Input Simulator Module (LT) |
| IC693ACC301 | Replacement Battery, CPU & PCM (qty 2) |
| IC693ACC302 | High capacity battery pack. The new Auxiliary Battery Pack (IC693ACC302) will enable Series 90-30 & Series 90-70 CPUs (except CPU374) to go up to 75 months (shelf life of 10 years ) of RAM memory backup w/no power & the CPU374 backup=15 mo |
| IC693ACC303 | Memory Card, 32 KBytes, Use With HHP (qty 1) |
| IC693ACC305 | EEPROM Chips (qty 4) |
| IC693ACC306 | EPROM Chips (qty 4) |
| IC693ACC307 | I/O Bus Terminator Plug |
| IC693ACC308 | Rack Adaptor Bracket, Series 90-30 10 Slot to 19" (Front Mount) |
| IC693ACC309 | Rack Adaptor Bracket, Series One 5 and 10 Slot Racks |
| IC693ACC310 | Filler Module, Blank Slot |
| IC693ACC311 | Terminal Blocks (qty 6) |
| IC693ACC315 | Battery Adapter Kit (battery not included) for CPU31* and CPU32* |
| IC693ACC316 | Connector Kit, 24 Pin, Qty (10), Solder Eyelet (For MDL654, 655, 752, 753) |
| IC693ACC317 | Connector Kit, 24 Pin, Qty (10), Crimp Type (For MDL654, 655, 752, 753) |
| IC693ACC318 | Connector Kit, 24 Pin, Qty (10), Ribbon Type (For MDL654, 655, 752, 753) |
| IC693ACC319 | Spare Parts Kit (I/O, CPU, PCM) |
| IC693ACC320 | Spare Parts Kit (Power Supply) |
| IC693ACC328 | Utility Update Software |
| IC693ACC329 | TBQC Base for IC693MDL645, IC693MDL646, and IC693MDL240 |
| IC693ACC330 | TBQC Base for IC693MDL740, IC693MDL742 |
| IC693ACC331 | TBQC Base for IC693MDL741 |
| IC693ACC332 | TBQC Base for IC693MDL940 |
| IC693ACC333 | TBQC Base for IC693MDL340 |
| IC693ACC334 | Module Connector for use with all 9030 terminal bases |
| IC693ACC335 | Axis Terminal Block for the Motion Mate DSM302 |
| IC693ACC336 | Auxiliary Terminal Block for the Motion Mate DSM302 |
| IC693ACC337 | TBQC Base for IC693MDL654/655/752/753 |
| IC693ACC338 | CPU364 FACEPLATE KIT CONTAINS 5 EACH FRONT PLASTIC AND LABELS |
| IC693ACC340 | Redundant Power Supply Base (RPSB) with 0.1 meter cable to connect to Power Supply Adapter module. Supports any Series 90-30 power supply. |
| IC693ACC341 | Redundant Power Supply Base with 0.5 meter cable to connect to Power Supply Adapter module. Supports any Series 90-30 power supply. |
| IC693ACC350 | Redundant Power Supply Adapter (RPSA) Module. The RPSA replaces the power supply on a CPU base or expansion base and connects to a Redundant Power Supply Base. |
| IC693ACC760 | Solenoind Valve Module Forcing Pendent |
| IC693ADC311 | CIMPLICITY 90-ADS Coprocessor (Repeat Systems) |
| IC693ADS301 | CIMPLICITY 90-ADS Package (First System) |
| IC693ALG222 | Analog Input, Voltage 16 Single/8 Differential Channels |
| IC693ALG222LT | Analog Input, Voltage 16 Single/8 Differential Channels (LT) |
| IC693ALG390 | Analog Output, Voltage, 2 Channels |
| IC693ALG390LT | Analog Output, Voltage, 2 Channels (LT) |
| IC693ALG392 | High Density Analog Output (8 Channels) |
| IC693ALG392LT | High Density Analog Output (8 Channels) (LT) |
| IC693ALG442 | Analog Combo Module 4IN/2OUT |
| IC693ALG442LT | Analog Combo Module 4IN/2OUT (LT) |
| IC693APU300 | High Speed Counter (HSC) |
| IC693APU300LT | High Speed Counter (HSC) (LT) |
| IC693APU301 | Axis Positioning Module (APM), 1 Axis |
| IC693APU302 | Axis Positioning Module (APM), 2 Axis |
| IC693APU305 | I/O Processor Module |
| IC693BEM320 | I/O Link Interface Module (Slave) |
| IC693BEM321 | I/O Link Interface Module (Master) |
| IC693BEM331 | Genius Bus Controller |
| IC693BEM331LT | Genius Bus Controller (supports I/O and Datagrams) (LT) |
| IC693CBK001 | Cable Kit for High Density I/O Modules (includes CBL327 and CBL328) |
| IC693CBK002 | Cable Kit for High Density I/O Modules (includes CBL329 and CBL330) |
| IC693CBK003 | Cable Kit for High Density I/O Modules (includes CBL331 and CBL332) |
| IC693CBK004 | Cable Kit for High Density I/O Modules (includes CBL333 and CBL334) |
| IC693CBL300 | Cable, I/O Expansion, 1 Meter |
| IC693CBL301 | Cable, I/O Expansion, 2 Meters |
| IC693CBL302 | Cable, I/O Expansion, 15 Meters |
| IC693CBL303 | Cable, Hand Held Programmer (HHP), 2 Meters |
| IC693CBL304 | Cable, Port Expansion, Used With PCM300 |
| IC693CBL305 | Cable, Port Expansion, Used With PCM301, PCM311, and CMM311 |
| IC693CBL306 | Cable, Extension, 1 Meter (Use with MDL652-653, MDL750-751) |
| IC693CBL307 | Cable, Extension, 2 Meters (Use with MDL652-653, MDL750-751) |
| IC693CBL308 | Cable, Single Connector, 1 Meter (Use with MDL652-653, MDL750-751) |
| IC693CBL309 | Cable, Single Connector, 2 Meters (For MDL652-653, MDL750-751) |
| IC693CBL311 | Cable, APM300/MCS300 Digital I/O, 24 Pin, 3 Meters |
| IC693CBL312 | Cable, I/O Expansion, 0.15 Meters, Shielded |
| IC693CBL313 | Cable, I/O Expansion, 8 Meters |
| IC693CBL316 | Station Manager Serial Cable for Ethernet TCP/IP |
| IC693CBL324 | Cable, Terminal Board Connections for DSM302, 1 Meter |
| IC693CBL325 | Cable, Terminal Board Connections for DSM302, 3 Meters |
| IC693CBL327 | Cable, Left Side, One - 24 Pin 90 Degree Connector, 3 Meter |
| IC693CBL328 | Cable, Right Side, One - 24 Pin 90 Degree Connector, 3 Meter |
| IC693CBL329 | Cable, Left Side, Two - 24 Pin 90 Degree Connectors, 1 Meter |
| IC693CBL330 | Cable, Right Side, Two - 24 Pin 90 Degree Connectors, 1 Meter |
| IC693CBL331 | Cable, Left Side, Two - 24 Pin 90 Degree Connectors, 2 Meter |
| IC693CBL332 | Cable, Right Side, Two - 24 Pin 90 Degree Connectors, 2 Meter |
| IC693CBL333 | Cable, Left Side, Two - 24 Pin 90 Degree Connectors, .5 Meter |
| IC693CBL334 | Cable, Right Side, Two - 24 Pin 90 Degree Connectors, .5 Meter |
| IC693CDC200 | Series 90-30 CsCAN interface module. One CsCAN port and one programming port for network devices. |
| IC693CHS391 | Base, CPU, 10 Slots, Use With CPU331/CSE331 and above |
| IC693CHS391LT | Base, CPU, 10 Slots, Use With CPU331/CSE331 and above (LT) |
| IC693CHS392 | Base, Expansion, 10 Slots |
| IC693CHS392LT | Base, Expansion, 10 Slots (LT) |
| IC693CHS393 | Base, Remote Expansion, 10 Slots (700 ft.) |
| IC693CHS393LT | Base, Remote Expansion, 10 Slots (700 ft.) (LT) |
| IC693CHS397 | Base, CPU, 5 Slots, Use With CPU331/CSE331 and above |
| IC693CHS397LT | Base, CPU, 5 Slots, Use With CPU331/CSE331 and above (LT) |
| IC693CHS398 | Base, Expansion, 5 Slots |
| IC693CHS398LT | Base, Expansion, 5 Slots (LT) |
| IC693CHS399 | Base, Remote Expansion, 5 Slots (700 ft.) |
| IC693CHS399LT | Base, Remote Expansion, 5 Slots (700 ft.) (LT) |
| IC693CMM301 | Genius Communications Module, GCM (256 bits) |
| IC693CMM302 | Communication Module, Genius (1 Kbyte) GCM+ |
| IC693CMM302LT | Communication Module, Genius (1 Kbyte) GCM+ (no datagram support) (LT) |
| IC693CMM311 | Communications Module, CCM, RTU, SNP, and SNPx Protocols |
| IC693CMM311LT | Communications Module, CCM, RTU, SNP, and SNPx Protocols (LT) |
| IC693CMM321 | Ethernet Interface TCP/IP Module |
| IC693CPU311 | 5-Slot Base With CPU in base (6K Bytes User Program) |
| IC693CPU311LT | 5-Slot Base With CPU in base (6K Bytes User Program) (LT) |
| IC693CPU313 | 5-Slot Base With Turbo CPU in base (.6 msec), 1K Registers, (12K Bytes User Program) |
| IC693CPU313LT | 5-Slot Base With Turbo CPU in base (.6 msec), 1K Registers, (12K Bytes User Program) (LT) |
| IC693CPU323 | 10-Slot Base With Turbo CPU in base (.6 msec) 12K bytes User Program |
| IC693CPU323LT | 10-Slot Base With Turbo CPU in base (.6 msec) 12K bytes User Program (LT) |
| IC693CPU331 | CPU 331 Module (16K Bytes) |
| IC693CPU331LT | CPU 331 Module (16K Bytes) (LT) |
| IC693CPU340 | CPU 340 Module (32K Bytes user memory), 10K Registers, .3 msec/K |
| IC693CPU341 | CPU 341 Module (80K Bytes user memory), 10K Registers, .3 msec/K |
| IC693CPU350 | CPU 350 Module (32K Bytes user memory, 4K I/O, 8 Racks), no built-in Serial Ports .22msec/K |
| IC693CPU350LT | CPU 350 Module (32K Bytes user memory, 4K I/O, 8 Racks), no built-in Serial Ports .22msec/K (LT) |
| IC693CPU351 | CPU 351 Module (240K Bytes configurable user memory, 4K I/O, 8 Racks) two built-in Serial Ports .22msec/K |
| IC693CPU352 | CPU 352 Module (240K Bytes configurable user memory, 4K I/O, 8 Racks, Hardware FLOATING POINT MATH), two built-in Serial Ports .22msec/K |
| IC693CPU352LT | CPU 352 Module (240K Bytes configurable user memory, 4K I/O, 8 Racks, Hardware FLOATING POINT MATH), two built-in Serial Ports .22msec/K (LT) |
| IC693CPU360 | CPU 360 Module (240K Bytes configurable user memory, 4K I/O, 8 Racks), no built-in Serial Ports .22msec/K |
| IC693CPU360CA | Series 90-30 CPU360 with Conformal Coated. |
| IC693CPU360LT | CPU 360 Module (240K Bytes configurable user memory, 4K I/O, 8 Racks), no built-in Serial Ports .22msec/K (LT) |
| IC693CPU363 | CPU 363 Module (240K Bytes configurable user memory) |
| IC693CPU363LT | CPU 363 Module (240K Bytes configurable user memory) (LT) |
| IC693CPU364 | CPU 364 Module (240K Bytes configurable user memory), Embedded Ethernet |
| IC693CPU366 | CPU 366 Module (240K Bytes configurable Supports Profibus DP Master (Version 1 supported). One Profibus port and one RS-232 service port. |
| IC693CPU367 | CPU 367Module (240K Bytes configurable Supports Profibus DP Slave (Version 1 supported). One Profibus port and one RS-232 service port. |
| IC693CPU374 | CPU 374 Module (240K Bytes configurable user memory) The battery for the CPU is now included in the CPU backplane box, Embedded Ethrnet 10/100Mbs w/built-in switch. No serial ports. |
| IC693CPU374CA | Series 90-30 CPU374 Conformal Coated. |
| IC693CPU500 | Series 90-30 Cscape CPU supports 1,024 I/O. The processor can be programmed the same as the OCS products over the built-in network that supports CsCAN or DeviceNet Slave. |
| IC693CSE311 | Series 90-30 5-Slot State Logic CPU in base Model 311 |
| IC693CSE313 | Series 90-30 5-Slot State Logic CPU in base Model 313 |
| IC693CSE323 | Series 90-30 10-Slot State Logic CPU in base Model 323 |
| IC693CSE331 | Series 90-30 Modular State Logic CPU 331 |
| IC693CSE340 | Series 90-30 Modular State Logic CPU 340 |
| IC693DNM200 | DeviceNet Master |
| IC693DNS201 | DeviceNet Slave |
| IC693DSM302 | Series 90-30 Motion Mate DSM302 Motion Controller, 2 Axis |
| IC693DSM314 | Series 90-30 DSM314 Motion Controller, 1-4 axis |
| IC693DSM324 | DSM324i 4-axis motion controller for the Series90-30 |
| IC693LBR301 | 90-30 Documentation Library (paper manuals covering most options) |
| IC693MAR590 | Mixed I/O, 120Vac Input (8 points), Relay Output (8 points) |
| IC693MAR590LT | Mixed I/O, 120Vac Input (8 points), Relay Output (8 points) (LT) |
| IC693MCD001 | Demo case, Beta Series Servo |
| IC693MCM001 | Series 90-30 Digital Servo Interface Module |
| IC693MDL230 | 120 Vac Isolated Input (8 Points) |
| IC693MDL230LT | 120 Vac Isolated Input (8 Points) (LT) |
| IC693MDL231 | 240 Vac Isolated Input (8 Points) |
| IC693MDL231LT | 240 Vac Isolated Input (8 Points) (LT) |
| IC693MDL240 | 120 Vac Input (16 Points) |
| IC693MDL240LT | 120 Vac Input (16 Points) (LT) |
| IC693MDL241 | 24 Vac/Vdc Input (16 Points) |
| IC693MDL241LT | 24 Vac/Vdc Input (16 Points) (LT) |
| IC693MDL250 | 120 Vac Isolated Input (16 points). Module requires a terminal block IC694TBBx32 or IC693TBSx32). |
| IC693MDL260 | 32 Point 120VAC Input Module. Requires terminal block IC694TBxx32. |
| IC693MDL310 | 120 Vac Output, 0.5 Amp (12 Points) |
| IC693MDL330 | 120/240 Vac Output, 2 Amp (8 Points) |
| IC693MDL330LT | 120/240 Vac Output, 2 Amp (8 Points) (LT) |
| IC693MDL340 | 120 Vac Output, 0.5 Amp (16 Points) |
| IC693MDL340LT | 120 Vac Output, 0.5 Amp (16 Points) (LT) |
| IC693MDL350 | 120/240 Vac Isolated Output, 2 Amp (16 Points). Module requires a terminal block (IC694TBBx32 or IC693TBSx32). |
| IC693MDL390 | 120/240 Vac Isolated Output, 2 Amp (5 Points) |
| IC693MDL390LT | 120/240 Vac Isolated Output, 2 Amp (5 Points) (LT) |
| IC693MDL632 | 125 Vdc Input (8 Points) |
| IC693MDL632LT | 125 Vdc Input (8 Points) (LT) |
| IC693MDL634 | 24 Vdc Input, Negative/Positive Logic (8 Points) |
| IC693MDL634LT | 24 Vdc Input, Negative/Positive Logic (8 Points) (LT) |
| IC693MDL645 | 24 Vdc Input, Neg/Pos Logic (16 Points) |
| IC693MDL645LT | 24 Vdc Input, Neg/Pos Logic (16 Points) (LT) |
| IC693MDL646 | 24 Vdc Input, Neg/Pos Logic, 1 msec Filter (16 points) |
| IC693MDL646LT | 24 Vdc Input, Neg/Pos Logic, 1 msec Filter (16 points) (LT) |
| IC693MDL648 | 48VDC Input, Neg/Pos Logic, 1 msec filter, Neg/Pos Logic (16 points) |
| IC693MDL653 | 24 Vdc Input, Neg/Pos Logic, 2msec Filter (32 Points) |
| IC693MDL654 | 5/12 Vdc (TTL) Input, Neg/Pos Logic, (32 points) |
| IC693MDL654LT | 5/12 Vdc (TTL) Input, Neg/Pos Logic, (32 points) (LT) |
| IC693MDL655 | 24 Vdc Input, Neg/Pos Logic, 1 ms, (32 pts) |
| IC693MDL655LT | 24 Vdc Input, Neg/Pos Logic, 1 ms, (32 pts) (LT) |
| IC693MDL660 | 24VDC Input Module 32 point. The module requires a terminal block (IC694TBB032 box style or IC694TBS032 springclamp style terminal block).Terminal block is sold seperately. |
| IC693MDL730 | 12/24 Vdc Output, 2 Amp, Positive Logic (8 Points) |
| IC693MDL730LT | 12/24 Vdc Output, 2 Amp, Positive Logic (8 Points) (LT) |
| IC693MDL731 | 12/24 Vdc Output, 2 Amp, Negative Logic (8 Points) |
| IC693MDL731LT | 12/24 Vdc Output, 2 Amp, Negative Logic (8 Points) (LT) |
| IC693MDL732 | 12/24 Vdc Output, 0.5 Amp, Positive Logic (8 Points) |
| IC693MDL733 | 12/24 Vdc Output, 0.5 Amp, Negative Logic (8 Points) |
| IC693MDL734 | 125 Vdc Output, (6 Points) |
| IC693MDL734LT | 125 Vdc Output, (6 Points) (LT) |
| IC693MDL740 | 12/24 Vdc Output, 0.5 Amp, Positive Logic (16 Points) |
| IC693MDL740LT | 12/24 Vdc Output, 0.5 Amp, Positive Logic (16 Points) (LT) |
| IC693MDL741 | 12/24 Vdc Output, 0.5 Amp, Negative Logic (16 Points) |
| IC693MDL741LT | 12/24 Vdc Output, 0.5 Amp, Negative Logic (16 Points) (LT) |
| IC693MDL742 | 12/24 Vdc Output, 1 Amp, Positive Logic (16 Points), Fused |
| IC693MDL742LT | 12/24 Vdc Output, 1 Amp, Positive Logic (16 Points), Fused (LT) |
| IC693MDL748 | 48VDC Output, 0.5 Amps, Positive Logic (8 points) |
| IC693MDL750 | 12/24 Vdc Output, Negative Logic (32 Points) |
| IC693MDL751 | 12/24 Vdc Output, Positive Logic (32 Points) |
| IC693MDL752 | 5/12/24 Vdc (TTL) Output, Neg Logic, (32 points) |
| IC693MDL752LT | 5/12/24 Vdc (TTL) Output, Neg Logic, (32 points) (LT) |
| IC693MDL753 | 12/24 Vdc Output, Pos Logic (32 Pts) |
| IC693MDL753LT | 12/24 Vdc Output, Pos Logic (32 Pts) (LT) |
| IC693MDL754 | 12/24VDC Output (0.75 amps per point) Module 32 point. The module requires a terminal block (IC694TBB032 box style or IC694TBS032 spring clamp style terminal block). |
| IC693MDL760 | Solenoid Valve Output (11 Points)/ 24VDC Output ,0.5 Amp, Positive Logic (5 Points) |
| IC693MDL930 | Relay Output, Isolated, 4 Amp (8 Points) |
| IC693MDL930LT | Relay Output, Isolated, 4 Amp (8 Points) (LT) |
| IC693MDL931 | Relay Output, 8 Amp Form B/C contacts, Isolated in groups of 4 |
| IC693MDL931LT | Relay Output, 8 Amp Form B/C contacts, Isolated in groups of 4 (LT) |
| IC693MDL940 | Relay Output, 2 Amp (16 Points) |
| IC693MDL940LT | Relay Output, 2 Amp (16 Points) (LT) |
| IC693MDR390 | Mixed I/O, 24Vdc Input (8 points), Relay Output (8 points) |
| IC693MDR390LT | Mixed I/O, 24Vdc Input (8 points), Relay Output (8 points) (LT) |
| IC693MLX000 | Series 90-30 I/O Modules Label Kit (various quantities) |
| IC693NIU004 | Series 90-30 Ethernet NIU (Ethernet I/O) |
| IC693NIU004CA | Series 90-30 Ethernet NIU Conformal Coated. 10/100Mbit Ethernet. |
| IC693PBM200 | Profibus DP Master Module |
| IC693PBS201 | Profibus DP Slave Module |
| IC693PCM300 | Prog. Coproc. Mdl., 160 KB (35 KB Basic Prgm), w/Port Exp. Cbl. |
| IC693PCM300LT | Prog. Coproc. Mdl., 160 KB (35 KB Basic Prgm), w/Port Exp. Cbl. (LT) |
| IC693PCM300LTMP | Prog. Coproc. Mdl., 160 KB (35 KB Basic Prgm), w/Port Exp. Cbl. Modified for use by OEMs (LT) |
| IC693PCM300-MP | Prog. Coproc. Mdl., 160 KB (35 KB Basic Prgm), w/Port Exp. Cbl. Modified for use by OEMs |
| IC693PCM301 | Prog. Coproc. Mdl., 192 KB (47 KB Basic Prgm), w/Port Exp. Cbl. |
| IC693PCM301LT | Prog. Coproc. Mdl., 192 KB (47 KB Basic Prgm), w/Port Exp. Cbl. (LT) |
| IC693PCM311 | Prog. Coproc. Mdl., 640 KB (190 KB Basic Prgm), w/Port Exp. Cbl. |
| IC693PCM311LT | Prog. Coproc. Mdl., 640 KB (190 KB Basic Prgm), w/Port Exp. Cbl. (LT) |
| IC693PIF301 | PC/AT Interface (PCIF) to Series 90-30 I/O with software |
| IC693PIF350 | Series 90-30 I/O PCI Bus interface board. Enables users to connect Series 90-30 I/O to a PCI interface board. |
| IC693PIF400 | High Performance PC/AT Interface (PCIF) to Series 90-30 I/O with software |
| IC693PRG300 | Hand Held Programmer (HHP) With Cable & Manual |
| IC693PTM100 | Power Transducer Module (Includes module, interface, 0.5m cable) |
| IC693PTM101 | Power Transducer Module (includes module, interface, 1m cable) |
| IC693PWR321 | Power Supply, 120/240 Vac, 125 Vdc, Standard |
| IC693PWR321LT | Power Supply, 120/240 Vac, 125 Vdc, Standard (LT) |
| IC693PWR322 | Power Supply, 24/48 Vdc, Standard |
| IC693PWR322LT | Power Supply, 24/48 Vdc, Standard (LT) |
| IC693PWR328 | Power Supply, 48 Vdc, Standard |
| IC693PWR328LT | Power Supply, 48 Vdc, Standard (LT) |
| IC693PWR330 | Power Supply, 120/240 Vac, 125 Vdc, High Capacity |
| IC693PWR331 | Power Supply, 24 Vdc, High Capacity |
| IC693PWR332 | Power Supply, 12 Vdc input, 30-watt output, High Capacity |